## Slide 1
Autonomous System Project
Distributed ROS 2 Navigation Architecture
Team Number: #18
Course: MCTR1002 | Autonomous Systems
Authors: Y. Mohamed, B. Walid, S. Hany, S. Magdy, Y. Hesham, M. Shakweer
Welcome to our presentation on the Team 18 Autonomous System Project. We have developed a high-performance navigation stack using a distributed processing architecture.

## Slide 2
This project validates a highly effective, dual-board autonomous driving architecture. By distributing computational load between a Raspberry Pi 5 and Arduino Uno, we eliminated bottlenecks, ensuring crisp responses across complex track environments including straight tracks, obstacle-rich racing circuits, and high-curvature city routes.
EXECUTIVE SUMMARY
Our core objective was to create a reliable vehicle capable of navigating varied environments by separating high-level planning from low-level actuation.

## Slide 3
The Sense-Plan-Act Framework
We implemented a modular architecture split into two main layers:
•
High-Level: Raspberry Pi 5 manages ROS 2 trajectory generation and Pure Pursuit calculations.
•
Low-Level: Arduino Uno handles PWM motor regulation and real-time sensor polling.
•
Communication: High-speed 115200 baud serial connection over USB.
DISTRIBUTED SYSTEM ARCHITECTURE
By assigning heavy geometric logic to the Pi 5 and critical timing tasks to the Arduino, we achieved a stable loop rate of 20 Hertz for lateral control.

## Slide 4
Computing
Raspberry Pi 5 (8GB) paired with Arduino Uno for dual-core task isolation.
Sensing
MPU6050 IMU for orientation and 11 PPR encoders for longitudinal tracking.
Actuation
JGA-25-370 Geared DC motor and high-torque steering servo for precise control.
HARDWARE COMPONENT STACK
Our hardware stack was chosen to balance power and precision. The Pi 5 gives us the headroom for future AI-based planning.

## Slide 5
Dead Reckoning
Local position tracking is maintained via Euler integration on the MCU to minimize latency.
Key Features
•
High-rate position updates at 100Hz.
•
Synchronized coordinate frames between Pi and Arduino.
•
MPU6050 yaw drift compensation via pre-sampled bias thresholds.
LOCAL STATE ESTIMATION
Accurate localization is the foundation of navigation. We use standard dead reckoning formulas updated in real-time.

## Slide 6
To mitigate sensory noise and chassis vibrations, we implemented first-order low-pass filters:
Speed & Heading Filter
•
Gyro Scaling: Calibrated with a 1.0256 factor to correct accumulated yaw drift.
•
Encoder Filtering: 0.943 calibration factor handles wheel slip errors.
DIGITAL SIGNAL FILTRATION
Raw data is often noisy. These filters ensure the control algorithms receive smooth, reliable input.

## Slide 7
Straight Track
Pure longitudinal tracking targeting theta=0 with boundary braking at 10m.
Racing Track
Predictive lane changes between y = ±0.25m to bypass static hazards.
City Track
22-point dense waypoint circuit with acute corners and varied tangents.
PATH PLANNING APPROACHES
Our system was tested across three scenarios, ranging from simple straight lines to complex urban layouts.

## Slide 8
Geometric Path Tracking
We use a speed-scaled lookahead distance to identify the target coordinate on the trajectory.
PURE PURSUIT LATERAL CONTROL
Pure Pursuit allows for smooth steering by aiming for a lookahead point, naturally handling path curvature.

## Slide 9
Actuator | Input Source | Control Logic | Output Range
DC Motor | Serial (Vel) | Proportional Closed-Loop | PWM 0 - 255
Steering Servo | Serial (Angle) | Exponential Smoothing | 45° - 135°
Logic Layer | Filtered IMU/Encoder | BasePWM + Error Scaling | Real-time Adjust
ACTUATOR CONTROL LOGIC
The Arduino converts high-level commands into precise electrical signals for our motors and servos.

## Slide 10
Trajectory Stability
The city track lap demonstrates excellent cornering management.
•
Lap Completion: 100% success rate.
•
Yaw Accrual: Continuous accumulation reaching ~360° for a full lap.
•
Velocity: Maintained a consistent 0.185 m/s despite varied steering loads.
PERFORMANCE ANALYSIS: CITY TRACK
In our most complex test, the city circuit, the robot maintained a stable speed while accurately rounding sharp corners.

## Slide 11
Data confirms that the unified stack successfully minimizes errors across all physical environments.
EXPERIMENTAL RESULT SUMMARY
Quantitatively, our lateral error remained below 6 centimeters in all cases, which is well within our target safety margins.

## Slide 12
Thank you! Any Questions?
Accomplishments
Next Steps
•
Validated dual-board RPi-Arduino architecture.
•
Successful hazard avoidance and lane shifting.
•
Robust noise filtration for real-world sensing.
•
Migration to Model Predictive Control (MPC).
•
Integration of obstacle detection via LiDAR/Vision.
•
Optimization for high-speed volatile environments.
CONCLUSION & FUTURE OUTLOOK
In conclusion, we've built a robust platform. Looking ahead, we plan to implement Model Predictive Control to further enhance high-speed stability.